## Slide 2
Autonomous System

## Slide 3
RULES
  No side talks
  Phones are in silent mode
  Questions after each slide
  Take permission before leaving
  There will be a break during the session if you want to eat or drink
  Make sure to take notes about what is discussed

## Slide 4
Session 5
“Motion planning”

## Slide 5
About the instructor
Name : Zaynab Ahmad
Mechatronics lvl 200
Autonomous committee Member 2023

## Slide 6
Agenda
Introduction to planning
Why motion planning
Challenges in motion planning
Basic concepts 1- c- configuration space 2- state space 3- degree of freedom (DOF)
4- path vs trajectory
Types of motion planning
Recap on occupancy grid map and graph
Algorithms used in each type motion planning

## Slide 8: Motion planning
Getting to the location, getting by any obstacles, following any rules

## Slide 9: Motion planning
Navigating from S to G on the map
Low-level details are abstracted away
Ensure safe navigation by avoiding obstacles
Allows adaptation to dynamic and changing environments
The goal is to find the most efficient path (in terms of time and distance)

## Slide 10: Motion planning challenges
Complex environment urban settings with traffic , pedestrians ,cyclists , and diverse road conditions
Real-time decision making respond to rapidly changing situations delays or inefficient planning can effect safety and smooth operation

## Slide 11: Motion planning challenges
Uncertainty and prediction
Optimality VS. Real time efficiency
Legal and ethical considerations
Sensor limitations
Human – robot interaction

## Slide 12: Basic concepts
C-configuration space
State space
Degree of freedom
Path VS trajectory

## Slide 13: Basic concepts:
Degree of freedom (DOF)
Numbers of independent parameters or variables required to fully describe the configuration or state of the system

## Slide 14: Basic concepts:
Degree of freedom (DOF)

## Slide 15: Basic concepts:
State space
A mathematical representation that describes all complete set of possible states or configurations of a system at a specific moment

## Slide 16
Basic concepts: Configuration space
A mathematical abstraction that represents all possible configurations or states that a system, such as a self-driving car can take, considering its degrees of freedom and constraints

## Slide 18
Path VS trajectory
Path a path represents a series of connected points in space that describe the desired route from the initial to the final position
Focus on geometry and do not include time or velocity data useful for high-level planning, providing a general route to follow

## Slide 19
Path VS trajectory
Trajectory a trajectory extends the concepts of a path by adding time and velocity information to each point, resulting in a dynamic sequence of states
Specify not only where the system should be but also how it should get there at what speed
ensuring smooth and precise motion execution

## Slide 20
Recap on occupancy grid
Is a 2D representation of the environment
It is very similar to the grayscale image
Occupancy probability
Assumptions 1- static environment 2- independent cells 3- a place can be either occupied or free

## Slide 21
Recap on occupancy grid

## Slide 22
Recap on graph
Concepts
Directed VS undirected graphs
Weighted graphs
Configuration space graphs
Graph search algorithms
Optimally VS completeness

## Slide 23: Types of motion planning
Motion planning broke into hierarchy of some problems
Mission planners focuses on mop-level navigation
Behavioral planning focuses on other agents, rules of the road , driving behaviors
Local planner focuses on generating feasible, collision-free path

## Slide 24: Mission planner(route selection)
Mission planners focuses on mop-level navigation
can be solved with graph-based methods (A*, Dijkstra's)

## Slide 25
Works on both directed and undirected graphs
Single source shortest path (SSSP)
Non-negative edge weights
Uses cost function(g(n))
Time complexity: O(E*log(v))
Steps : 1- update estimates 2- choose the next vertex
Mission planner –Dijkstra's
Pseudo-code
For each vertex V :
Dist[V]=∞ prev[V]=none
Dist[source]=0
Set all vertices to unexplored
While destination is not explored :
V = least_valued unexplored vertex set V to explored
For each edge (V,W):
If dist[V]+len(V,W)<dist[W]:
Dist[W] =Dist[V]+len(V,W) prev[W]=V

## Slide 26
Works on both directed and undirected graphs
Single source shortest path (SSSP)
Non-negative edge weights
Uses cost function (g(n)) and heuristic (h(n))
Time complexity: O(E*log(v))
Steps : 1- update estimates 2- choose the next vertex
Mission planner –A*
Pseudo-code
For each vertex V:
dist[V] = ∞ # Cost
prev[V] = none
heuristic[V] = heuristic_estimate(V, goal) # Heuristic
dist[source] = 0
Set all vertices to unexplored
While destination is not explored:
V = unexplored vertex with the lowest dist[V] + heuristic[V] value
Set V to explored
For each edge (V, W):
tentative_dist = dist[V] + len(V, W)
if tentative_dist < dist[W]:
dist[W] = tentative_dist
prev[W] = V

## Slide 27
Mission planner –optimization of algorithms
A* algo
A* optimization with epsilon

## Slide 28: Behavior planner
The behavior planner decides when it is safe to proceed
Takes pedestrians, vehicles, cyclists into consideration
Also looks at regulatory elements, such as traffic lights and stop signs

## Slide 29
Composed of states and transitions
    States are based on perception of surroundings
    Transitions are based on inputs from the driving scenario eg, stop lights changing color
FSM is memoryless
  Transition only depend on input and current state, and not past state sequence
Behavioral planner -Finite state machines

## Slide 30
Rule based system use a hierarchy of rules to determine output behavior
Rules are evaluated based on logical predicates
Higher priority rules have precedence
Behavioral planner –rule based

## Slide 31
Behavioral planner –Reindorsement learning

## Slide 32: Local planner
Local planning focuses on generating feasible, collision-free paths and comfortable velocity profiles
Decomposed into path planning and velocity profile generation

## Slide 33
Rapidly exploring the state space to find feasible trajectories.
Handling dynamic environments and real-time decision-making
There are two approaches (single-query and multiple-Query)
Balancing exploration (finding new paths) and exploitation (refining known paths).
Sampling based

## Slide 34: RRT

## Slide 36
Thank You